## Slide 1: Enhancing Mobile Apps to Use Sensor Hubs without Programmer Effort
Haichen Shen, Aruna Balasubramanian, Anthony LaMarca, David Wetherall

## Slide 2: Continuous sensing apps
Participatory sensing:
MobiPerf
Healthcare apps:
Ambulation
Lifestyle monitoring:
BeWell, Acoustic
Step Counting
Fall Detection
Driver Monitor
Theft Detection
Notes: Ambulation: a health monitoring application to monitor patients with mobility-affecting chronic diseases such as Parkinsons

## Slide 3: But it drains the battery
  Problem: CPU frequently wakes up to process sensor data
Notes: It is neither the sensors nor the computation that make these applications battery drainers

## Slide 4: Sensor hub: low power processor
Apple M7
Intel Merrifield
TI’s Tiva
~1.5 mW at 2MHz
Notes: Change the 1.5mW

## Slide 5: Existing approaches
APIs
Provided by software company
Easy to program
Only support a set of pre-defined events
Require programmer effort
Hardware SDK
Provided by hardware manufacturer
Full control of sensor hub
Compatibility
Require programmer effort
Notes: Android API vs Hardware SDK
In a seesaw
Requires programmer effort, cannot be used
  Apps developed in one vendor’s environment will not work in another’s and vice versa

## Slide 6: MobileHub: leverage sensor hub without programmer effort
Optimized app: Same semantics,
but more energy efficient
MobileHub
System
Analyze app and rewrite binary

## Slide 7: MobileHub example
Trigger
Steps:
0
No change to app semantics
CPU
Sensor
Display
Trigger
0
CPU
Sensor
Display
1
[Idle]
[Active]
1
MobileHub
CPU idle for longer
  Challenge: How does MobileHub know when the application needs to be triggered?
App
Notification
Steps:
Notes: If the app doesn’t have passive state, you cant help the app

## Slide 8: System Overview
Step 3a Sensor hub program: Implement the classifier in the sensor hub, corresponding to the app
Step 2 Learning: Learn how change in sensor values result in app notifications
Step 3b Application rewriting: Rewrite app to offload sensing to the sensor hub
Step 1 Dynamic taint tracking: Track app notifications for a series of sensor inputs
Optimized
app
Original
app
Step 0: Sensor traces
Taint
log
Classifier
model
Sensor parameter
MobileHub
System
Notes: Remove animation

## Slide 9: System overview
Step 3a Sensor hub program: Implement the classifier in the sensor hub, corresponding to the app
Step 2 Learning: Learn how change in sensor values result in app notifications
Step 3b Application rewriting: Rewrite app to offload sensing to the sensor hub
Step 1 Dynamic taint tracking: Track app notifications for a series of sensor inputs
Optimized
app
Original
app
Step 0: Sensor traces
Taint
log
Classifier
model
Sensor parameter
MobileHub
System

## Slide 10: Taint tracking
To track the flow of sensor data during the runtime and capture app notifications
void onSensorChange(sensorEvent){
X = sensorEvent.val;
Y = (X + 1) / 2;
if (Y > THRESHOLD) {
stepCounter++;
display(stepCounter);
}
}
Taint tag
Taint tag
Taint Source
Explicit Information Flow
Implicit Information Flow
Taint tag
Taint Sink
Taint tag
Notes: - Definition of taint tracking?

## Slide 11: Challenge: implicit flow
Most taint tracking platforms only track explicit flow
  Without implicit flow tracking, we could only track 20% of triggers for sensing apps
  Extend TaintDroid [Enck_OSDI2010] to track implicit flow

## Slide 12: Implicit flow tracking example
void onSensorChange(sensorEvent){
X = sensorEvent.val;
Y = (X + 1) / 2;
tag = getTaintTag(Y);
if (Y > THRESHOLD) {
stepCounter++;
Taint(stepCounter, tag);
display(stepCounter);
}
}
Taint tag
Taint tag
Taint Block
TAINT
CAPTURED
  Use static analysis to identify all taint blocks and instrument the app binary automatically.

## Slide 13: System overview
Step 3a Sensor hub program: Implement the classifier in the sensor hub, corresponding to the app
Step 2 Learning: Learn how change in sensor values result in app notifications
Step 3b Application rewriting: Rewrite app to offload sensing to the sensor hub
Step 1 Dynamic taint tracking: Track app notifications for a series of sensor inputs
Optimized
app
Original
app
Step 0: Sensor traces
Taint
log
Classifier
model
Sensor parameter
MobileHub
System

## Slide 14: Learning a buffer policy
Hard to use a classifier to model the app logic
Simply learn the statistical properties and distinguish between idle and active periods
Trigger
Time
Active
Idle
Label

## Slide 15: Goal: find a proper buffer size
Precisely predict active and idle periods
Reduce the number of notification delays
Trigger
Time
Buffer
Buffer
More to save
Notification delay!
Buffer

## Slide 16: Implementation
Implemented in Android
  Taint tracking
  Interface with sensor hub
  App binary rewriting
Prototype
  Implemented classifier on sensor hub

## Slide 17: End-to-end measurement
Notes: 5 minutes: 30 seconds stationary and manually moving it for 30 seconds in turn
22J vs 84J (almost 1/4)
Sensor hub power consumpt: 0.55J, 2.5%

## Slide 18: Trace-driven evaluation
Trace collection from 21 participants
  10 traces for sleeping, driving, and daily life
  5 traces for other activities
Downloaded 20 apps from Google Play
Notes: Trace contains a series of sensor input

## Slide 19
Name | Google Play Store ID | Task | Sensor
nWalk | pl.rork.nWalk | Step counting | Accelerometer
pedometer | bagi.levente.pedometer | Step counting | Accelerometer
stepcounter | Stepcounter.Step | Step counting | Accelerometer
appsone | net.appsone.android.pedometer | Step counting | Accelerometer
virtic | jp.virtic.apps.WidgetManpok | Step counting | Accelerometer
walking | cha.health.walking | Step counting | Accelerometer
lodecode | com.lodecode.metaldetector | Metal detector | Magnetometer
imkurt | com.imkurt.metaldetector | Metal detector | Magnetometer
tdt | com.tdt.magneticfielddetector | Metal detector | Magnetometer
multunus | com.multunus.falldetector | Fall detector | Accelerometer
iter | com.iter.falldetector | Fall detector | Accelerometer
t3lab | it.t3lab.fallDetector | Fall detector | Accelerometer
fall | com.fall | Fall detector | Accelerometer
jietusoft | com.jietusoft.earthquake | Earthquake detector | Accelerometer
vibration | ycl.vibrationsensor | Earthquake detector | Orientation
posvic | cz.posvic.fitnessbar.sleeptrack | Sleep monitoring | Gyroscope
myway | myway.project.sleepmanagement | Sleep monitoring | Accelerometer
driving | jp.co.noito.Accelerometer | Driver monitoring | Accelerometer
motion | com.app.accelerometer | Motion detector | Accelerometer
thefthead | com.thefthead.appfinalsettings | Theft detector | Accelerometer

## Slide 20: Methodology
Run each app on the phone receiving sensor values from a trace file
Trace file embeds the buffering policy
Power Accounting:
Measure the power consumption of phone
Deduct the standby power consumption

## Slide 21: Evaluation
Does MobileHub reduce power consumption for sensing applications?
How much delay does MobileHub cause in the app notifications?

## Slide 22: Energy improvement
Notes: Average of 3 traces for each app
improve the power consumption by a median of 74%
Taking out the metal apps, mobilehub improves power consumption by 70% in average

## Slide 23: Notification delay
App | Task | #Delay/#Notifications | Max delay (s)
nWalk | Step Counting | 1/3914 | 1.86
imkurt | Fall Detection | 2/142 | 0.98
posvic | Sleep Monitor | 1/36 | 0.64
thefthead | Anti-theft | 6/65 | 2.80
Notification is delayed by at least 0.5s
Notes: Across all apps, 1.5% notifications are delayed
Max delay is less than 1 sec in 80% of cases
- Why 0.5 second ?

## Slide 24: Conclusion
Design and implement MobileHub that rewrites application without programmer effort
Experiment with 20 sensing apps, and reduce power consumption by 74% in median
MobileHub delays 1.5% app notification across all apps on average

## Slide 25: Thank you!

## Slide 26: Back up

## Slide 27: Sensor Hub Service
Android Binder
Sensor Hub Service
Comm. Manager
Sensor Hub
Sensor Distributor
App
Hub Binder
Sensor Listener
App
Hub Binder
Sensor Listener

## Slide 28: Dynamic vs static buffer